## Slide 1: EDES 301 Window to Another World Proposal
Feb 22, 2026
Clay

## Slide 2: Background Information
For this project, I’d like to create a piece of art that is responsive to changes in rotation by showing different ‘slices’ of a 360 degree image. This is inspired by a cool build I saw of this Fluid Simulation Pendant that swishes the fluid around given detected movements by the IMU.
I will need a tool to turn a 360 degree image into a 2d ‘slice’ given my detected IMU angle (which should be reasonably simple, something I can code myself) and a tool to turn an image into a 32x32 LED matrix output (can use this tool? or this tool? to experiment. along with some hardware interface). Probably going to use some sort of dithering / data compression technique (ideally, the change as the device is moved around will give the viewer the ability to infer greater resolution of the image than the actual 32 x 32 pixel matrix would normally permit)

## Slide 3: System Block Diagram
PocketBeagle
GY-521 MPU6050
IMU Module
Adafruit
Model 607
32 x 32 LED Matrix
GPIO Pins
1 - 13
I2C(3.3V)
x4 Buttons
GPIO Pins 14-18
GPIO Pin 14
HCW-KC1206 Buzzer
3.3v - 5v
Level Shifter

## Slide 4: Power Block Diagram
PocketBeagle
GY-521 MPU6050
IMU Module
Adafruit
Model 607
32 x 32 LED Matrix
Data (No Power)
GPIO Pins 1-8 @ 5V
Data and Power
(3.3V VCC).
Total of 4 connections:
2 for I2C, VCC, GND
5V @ 5A External Power Supply
TXS0108E
3.3v - 5v
Level Shifter
GPIO Pins 1-8 @ 3.3V
VA @ 3.3V
VB @ 5V
Data (No Power)
GPIO Pins 8-13 @ 5V
TXS0108E
3.3v - 5v
Level Shifter
GPIO Pins 8-14 @ 3.3V
VA @ 3.3V
VB @ 5V
HCW-KC1206 Buzzer
3.3v - 5v
Level Shifter
GPIO Pin 14 @ 5V
GPIO Pins 14-18 @ 3.3V
x4 Buttons

## Slide 5: Components / Budget
Component | EDES301 to Buy? | Cost
32 x 32 Matrix (https://www.adafruit.com/product/607) | Yes | 29.95
IMU Module (https://www.amazon.com/dp/B09Q2SGF3R) | Yes | 2.10
(x2) Level Shifter (https://www.amazon.com/dp/B09R1QG957) | Yes | 3.2 (1.6 each)
(x4) Button | No | 
Buzzer | No | 
See Next Slide for Instructions